DIGITAL LOGIC
DIGITAL LOGIC
Multisim Lab Presentation
By J. Mathenge

---
Sample Task
Sample Task
Design a synchronous counter that uses the T-flip flop to count through the sequences 0,2,4,6 then repeats.
Solution:
Step 1: Start with a state diagram which shows the states that the flip flop should go through.
Map all the unused numbers to a given number on the state diagram.
1,3,5,7
0
2
6
4

---
Step 2: Determining the number of bits (flip flops) to use.
Check the largest digit in the counting sequence. For this case it is 6. In binary 6 is written as 110. We shall need a three bit system for this counter
Step 3: Show the truth table for the flip flop you are to use:

---
Step 4: Expand the truth table to get the characteristic table.
Step 5: From the characteristic table we can be able to get the excitation table for the flip flop.
0	0	0
0	1	1
1	0	1
1	1	0
0	0	0
0	1	1
1	0	1
1	1	0

---
Step 6:
				+	+
0	0	0	0	0	1	0	0	1	0
1	0	0	1	0	0	0	0	0	1
2	0	1	0	1	0	0	1	1	0
3	0	1	1	0	0	0	0	1	1
4	1	0	0	1	1	0	0	1	0
5	1	0	1	0	0	0	1	0	1
6	1	1	0	0	0	0	1	1	0
7	1	1	1	0	0	0	1	1	1

---
Step 7: Draw the k-maps for T3, T2, and T1.
T3
K-Map
	00	01	11	10
0	0	1	1	0
1	0	0	1	1

---
Step 7: Draw the k-maps for T3, T2, and T1.
	00	01	11	10
0	1	1	1	1
1	0	1	1	0
T2
K-Map

---
Step 7: Draw the k-maps for T3, T2, and T1.
Draw the circuit/ implement it on NI Multisim.
	00	01	11	10
0	0	0	0	0
1	1	1	1	1
T1
K-Map

---
Below are some IDs of the components you might need on Multisim:
Component	ID
1. JK Flip Flop	7476N
2. AND Gate	7408J
3. OR Gate	7432N

---
*End of session*

---
Questions….?